## Slide 1
RKTiwary
COA -IS ZC353

## Slide 2
Chapter 9
Computer Arithmetic
Notes: We begin our examination of the processor with an overview of the arithmetic and
logic unit (ALU). The chapter then focuses on the most complex aspect of the ALU,
computer arithmetic.

## Slide 3: Arithmetic & Logic Unit (ALU)
Part of the computer that actually performs arithmetic and logical operations on data
All of the other elements of the computer system are there mainly to bring data into the ALU for it to process and then to take the results back out
Based on the use of simple digital logic devices that can store binary digits and perform simple Boolean logic operations
Notes: The ALU is that part of the computer that actually performs arithmetic and logical
operations on data. All of the other elements of the computer system—control unit,
registers, memory, I/O—are there mainly to bring data into the ALU for it to process
and then to take the results back out. We have, in a sense, reached the core or
essence of a computer when we consider the ALU.

## Slide 4: ALU Inputs and outputs
Fig 9.1
Notes: Figure 9.1 indicates, in general terms, how the ALU is interconnected with
the rest of the processor. Operands for arithmetic and logic operations are presented
to the ALU in registers, and the results of an operation are stored in registers.
These registers are temporary storage locations within the processor that are
connected by signal paths to the ALU . The ALU may also set
flags as the result of an operation. For example, an overflow flag is set to 1 if the
result of a computation exceeds the length of the register into which it is to be stored.
The flag values are also stored in registers within the processor. The processor
provides signals that control the operation of the ALU and the movement of the
data into and out of the ALU.
The flag values are also stored in registers within the processor. The processor provides
signals that control the operation of the ALU and the movement of the data
into and out of the ALU.

## Slide 5: Integer Representation
In the binary number system arbitrary numbers can be represented with:
  The digits zero and one
  The minus sign (for negative numbers)
  The period, or radix point (for numbers with a fractional component)
  For purposes of computer storage and processing we do not have the benefit of special symbols for the minus sign and radix point
  Only binary digits (0,1) may be used to represent numbers
Notes: In the binary number system, arbitrary numbers can be represented with just the
digits zero and one, the minus sign (for negative numbers), and the period, or radix
point (for numbers with a fractional component).
For purposes of computer storage and processing, however, we do not have the benefit
of special symbols for the minus sign and radix point. Only binary digits (0 and 1)
may be used to represent numbers. If we are limited to nonnegative integers, the
representation is straightforward.

## Slide 6: Signed Nos 2’s complement representation
Eg +6= 0110
-6= 1010

## Slide 7
Consider any binary number in 2’s complement
101101

## Slide 8
Consider any binary number in 2’s complement
101101
= -26-1.1 + 24.0 + 23.1 + 22.2 + 21.0+ 20.1

## Slide 9
Consider any binary number in 2’s complement
101101
= -26-1.1 + 24.0 + 23.1 + 22.1 + 21.0+ 20.1
=-32 + 0 + 8 + 4 + 0 + 1= -19

## Slide 10
Consider any binary number in 2’s complement
101101
= -26-1.1 + 24.0 + 23.1 + 22.1 + 21.0+ 20.1
=-32 + 0 + 8 + 4 + 0 + 1= -19
The 2’s complement of 101101 is 010011= 19

## Slide 11
Consider any binary number in 2’s complement
101101
= -26-1.1 + 24.0 + 23.1 + 22.1 + 21.0+ 20.1
=-32 + 0 + 8 + 4 + 0 + 1= -19
The 2’s complement of 101101 is 010011= 19
Now if a 1 is appended then 1101101 ?

## Slide 12
Consider any binary number in 2’s complement
101101
= -26-1.1 + 24.0 + 23.1 + 22.1 + 21.0+ 20.1
=-32 + 0 + 8 + 4 + 0 + 1= -19
The 2’s complement of 101101 is 010011= 19
Now if a 1 is appended then 1101101 ?
1101101= -27-1.1 + 25.1 + 24.0 + 23.1 + 22.1+ 21.0 + 20.1
= -64+ 32 +0 + 8 + 4 + 0 + 1
= -19

## Slide 13: Addition and Subtraction
OVERFLOW RULE: If two numbers are added, and they are both positive or both negative, then overflow occurs if and only if the result has the opposite sign.

## Slide 14: Addition and Subtraction
SUBTRACTION RULE: To subtract one number (subtrahend) from another (minuend), take the twos complement (negation) of the subtrahend and add it to the minuend.

## Slide 15: Block Diagram of Hardware for Addition and Subtraction
OF= Overflow bit
SW =Switch (select addition or subtraction)

## Slide 16: Multiplication of UNSIGNED INTEGERS
1. Multiplication involves the generation of partial products, one for each digit in the multiplier. These partial products are then summed to produce the final product.
2. The partial products are easily defined. When the multiplier bit is 0, the partial product is 0.When the multiplier is 1, the partial product is the multiplicand.
3. The total product is produced by summing the partial products. For this operation, each successive partial product is shifted one position to the left relative to the preceding partial product.
4. The multiplication of two n-bit binary integers results in a product of up to 2n bits in length (e.g., 11 X 11=1001).

## Slide 17: Multiplication of UNSIGNED INTEGERS

## Slide 18: Multiplication of UNSIGNED INTEGERS

## Slide 19: Multiplication of UNSIGNED INTEGERS
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial value | 

## Slide 20: Multiplication of UNSIGNED INTEGERS
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial value | 
0 | 1011 | 1101 | 1011 | Add | First cycle
0 | 0101 | 1110 | 1011 | Shift | 

## Slide 21: Multiplication of UNSIGNED INTEGERS
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial value | 
0 | 1011 | 1101 | 1011 | Add | 1st cycle
0 | 0101 | 1110 | 1011 | Shift | 
0 | 0010 | 1111 | 1011 | shift | 2nd cycle

## Slide 22: Multiplication of UNSIGNED INTEGERS
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial value | 
0 | 1011 | 1101 | 1011 | Add | 1st cycle
0 | 0101 | 1110 | 1011 | Shift | 
0 | 0010 | 1111 | 1011 | shift | 2nd cycle
0 | 1101 | 1111 | 1011 | Add | 

## Slide 23: Multiplication of UNSIGNED INTEGERS
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial value | 
0 | 1011 | 1101 | 1011 | Add | 1st cycle
0 | 0101 | 1110 | 1011 | Shift | 
0 | 0010 | 1111 | 1011 | shift | 2nd cycle
0 | 1101 | 1111 | 1011 | Add | 3rd cycle
0 | 0110 | 1111 | 1011 | shift | 

## Slide 24: Multiplication of UNSIGNED INTEGERS
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial value | 
0 | 1011 | 1101 | 1011 | Add | 1st cycle
0 | 0101 | 1110 | 1011 | Shift | 
0 | 0010 | 1111 | 1011 | shift | 2nd cycle
0 | 1101 | 1111 | 1011 | Add | 3rd cycle
0 | 0110 | 1111 | 1011 | shift | 
1 | 0001 | 1111 | 1011 | Add | 

## Slide 25: Multiplication of UNSIGNED INTEGERS
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial value | 
0 | 1011 | 1101 | 1011 | Add | 1st cycle
0 | 0101 | 1110 | 1011 | Shift | 
0 | 0010 | 1111 | 1011 | shift | 2nd cycle
0 | 1101 | 1111 | 1011 | Add | 3rd cycle
0 | 0110 | 1111 | 1011 | shift | 
1 | 0001 | 1111 | 1011 | Add | 4th cycle
0 | 1000 | 1111 | 1011 | Shift | 143

## Slide 26: Multiplication of SIGNED INTEGERS
11 (1011) by 13 (1101) to get 143 (10001111)
-5(1011) times -3 (1101) equals -113 (10001111)

## Slide 27: Booth Multiplier

## Slide 28: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value

## Slide 29: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M

## Slide 30: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 

## Slide 31: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M

## Slide 32: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M
11110 | 00001 | 0 | 11000 | 

## Slide 33: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M
11110 | 00001 | 0 | 11000 | 
00110 | 00001 | 0 | 11000 | A-M

## Slide 34: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M
11110 | 00001 | 0 | 11000 | 
00110 | 00001 | 0 | 11000 | A-M
00011 | 00000 | 1 | 11000 | 

## Slide 35: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M
11110 | 00001 | 0 | 11000 | 
00110 | 00001 | 0 | 11000 | A-M
00011 | 00000 | 1 | 11000 | 
11011 | 00000 | 1 | 11000 | A-M

## Slide 36: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M
11110 | 00001 | 0 | 11000 | 
00110 | 00001 | 0 | 11000 | A-M
00011 | 00000 | 1 | 11000 | 
11011 | 00000 | 1 | 11000 | A-M
11101 | 10000 | 0 | 11000 | 

## Slide 37: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M
11110 | 00001 | 0 | 11000 | 
00110 | 00001 | 0 | 11000 | A-M
00011 | 00000 | 1 | 11000 | 
11011 | 00000 | 1 | 11000 | A-M
11101 | 10000 | 0 | 11000 | 
11110 | 11000 | 0 | 11000 | shift

## Slide 38: Multiplication of -8 X 5
01 A+M
10 A-M
A | Q(multiplier) | Q-1 | M(Multiplicand | Comments
00000 | 00101 | 0 | 11000 | Initial value
01000 | 00101 | 0 | 11000 | A-M
00100 | 00010 | 1 | 11000 | 
11100 | 00010 | 1 | 11000 | A+M
11110 | 00001 | 0 | 11000 | 
00110 | 00001 | 0 | 11000 | A-M
00011 | 00000 | 1 | 11000 | 
11011 | 00000 | 1 | 11000 | A-M
11101 | 10000 | 0 | 11000 | 
11110 | 11000 | 0 | 11000 | shift
11110 | 11000 | -40 | -512+472 | Final result

## Slide 39
The basic grammar school division algorithm
Division Algorithm and Hardware
Dividend = Quotient x Divisor + Remainder
The Divisor register, ALU, and Remainder register are all 64 bits wide, with only the Quotient register being 32 bits.
The 32-bit divisor starts in the left half of the Divisor register and is shifted right 1 bit each iteration.
The remainder is initialized with the dividend. Control decides when to shift the Divisor and Quotient registers and when to write the new value into the Remainder register.

## Slide 40
2a: shift the quotient register to the left , setting up the new rightmost bit to 1
it takes n + 1 steps to get the proper quotient and remainder

## Slide 41: Division 7/2
Shift left logical (sll)

## Slide 42
n | step | Quotient | Divisor | remainder
0 | Initial value | 0000 | 0100 0000 | 0000 1001
9/4

## Slide 43
n | step | Quotient | Divisor | remainder
0 | Initial value | 0000 | 0100 0000 | 0000 1001
1 | 1: Rem= Rem-Div | 0000 | 0100 0000 | 1100 1001
9/4

## Slide 44
n | step | Quotient | Divisor | remainder
0 | Initial value | 0000 | 0100 0000 | 0000 1001
1 | 1: Rem= Rem-Div | 0000 | 0100 0000 | 1100 1001
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0100 0000 | 0000 1001

## Slide 45
n | step | Quotient | Divisor | remainder
0 | Initial value | 0000 | 0100 0000 | 0000 1001
1 | 1: Rem= Rem-Div | 0000 | 0100 0000 | 1100 1001
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0100 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0010 0000 | 0000 1001

## Slide 46
n | step | Quotient | Divisor | remainder
0 | Initial value | 0000 | 0100 0000 | 0000 1001
1 | 1: Rem= Rem-Div | 0000 | 0100 0000 | 1100 0000
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0100 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0010 0000 | 0000 1001
2 | 1: Rem= Rem-Div | 0000 | 0010 0000 | 1110 1001
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0010 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0001 0000 | 0000 1001

## Slide 47
n | step | Quotient | Divisor | remainder
0 | Initial value | 0000 | 0100 0000 | 0000 1001
1 | 1: Rem= Rem-Div | 0000 | 0100 0000 | 1100 0000
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0100 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0010 0000 | 0000 1001
2 | 1: Rem= Rem-Div | 0000 | 0010 0000 | 1110 1001
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0010 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0001 0000 | 0000 1001
3 | 1: Rem= Rem-Div | 0000 | 0001 0000 | 1111 1001
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0001 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0000 1000 | 0000 1001

## Slide 48
n | step | Quotient | Divisor | remainder
0 | Initial value | 0000 | 0100 0000 | 0000 1001
1 | 1: Rem= Rem-Div | 0000 | 0100 0000 | 1100 0000
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0100 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0010 0000 | 0000 1001
2 | 1: Rem= Rem-Div | 0000 | 0010 0000 | 1110 1001
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0010 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0001 0000 | 0000 1001
3 | 1: Rem= Rem-Div | 0000 | 0001 0000 | 1111 1001
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0000 | 0001 0000 | 0000 1001
 | 3: Shift Div Right | 0000 | 0000 1000 | 0000 1001
4 | 1: Rem= Rem-Div | 0000 | 0000 1000 | 0000 0001
 | 2a: Rem>0 => sll Q, Q0=1 | 0001 | 0000 1000 | 0000 0001
 | 3: Shift Div Right | 0001 | 0000 0100 | 0000 0001
5 | 1: Rem= Rem-Div | 0001 | 0000 0100 | 1111 1101
 | 2b: Rem<0 => +Div, sll Q, Q0=0 | 0010 | 0000 0100 | 0000 0001
 | 3: Shift Div Right | 0010 | 0000 0010 | 0000 0001

## Slide 49
Signed Division
Dividend = Quotient  Divisor + Remainder
Remember the signs of the divisor and dividend and then negate the quotient if the signs disagree.
Look at the example of
The 1st case is easy
+11 ÷ +5: Quotient = +2, Remainder = +1
Checking the results:
11 = 2 × 5 + (+1) = 10 + 1

## Slide 50
Signed Division
Dividend = Quotient  Divisor + Remainder
2nd case If we change the sign of the dividend, the quotient must change as well:
–11 ÷ +5: Quotient = –2
Rewriting our basic formula to calculate the remainder:
Remainder = (Dividend – Quotient × Divisor) = –11 – (–2 × +5)
= –11–(–10) = –1
So,
–11 ÷ +5: Quotient = –2, Remainder = –1

## Slide 51
Signed Division
Dividend = Quotient  Divisor + Remainder
Checking the results again:
–11 = –2 × 5 + (–1) = – 10 – 1
The same result is obtained if
–11 = –3 × 5 + (4) = – 15 + 4
absolute value of the quotient would then change
How to avoid this?

## Slide 52
Signed Division
Dividend = Quotient  Divisor + Remainder
This anomalous behavior is avoided by following the rule that the dividend and remainder must have the same signs, no matter what the signs of the divisor and quotient.
+11 –5: Quotient = –2, Remainder = +1
–11 –5: Quotient = +2, Remainder = –1
Thus the correctly signed division algorithm negates the quotient if the signs of the operands are opposite and makes the sign of the nonzero remainder match the dividend