## Slide 1
RKTiwary
COA - L5

## Slide 2: IMP Note to Self

## Slide 3: IMP Note to Students
It is important to know that just login to the session does not guarantee the attendance.
Once you join the session, continue till the end to consider you as present in the class.
IMPORTANTLY, you need to make the class more interactive by responding to Professors queries in the session.
Whenever Professor calls your number / name ,you need to respond, otherwise it will be considered as ABSENT

## Slide 4: Real Numbers
Numbers with fractions
Could be done in pure binary
  1001.1010 = 24 + 20 +2-1 + 2-3 =9.625
Where is the binary point?
Fixed?
  Very limited
Moving?
  How do you show where it is?

## Slide 5: Floating Point
Normalized scientific notation: single non-zero digit to the
left of the decimal (binary) point – example: 3.5 x 109
1.010001 x 2-5two = (1 + 0 x 2-1 + 1 x 2-2 + … + 1 x 2-6) x 2-5ten
A standard notation enables easy exchange of data between
machines and simplifies hardware algorithms – the
IEEE 754 standard defines how floating point numbers
are represented

## Slide 6: Sign and Magnitude Representation
Sign Exponent Fraction
1 bit 8 bits 23 bits
S
E
F
More exponent bits  wider range of numbers (not necessarily more
numbers – recall there are infinite real numbers)
More fraction bits  higher precision
Register value = (-1)S x F x 2E
Since we are only representing normalized numbers, we are
guaranteed that the number is of the form 1.xxxx..
Hence, in IEEE 754 standard, the 1 is implicit
Register value = (-1)S x (1 + F) x 2E

## Slide 7: Sign and Magnitude Representation
Sign Exponent Fraction
1 bit 8 bits 23 bits
S
E
F
Largest number that can be represented:
Smallest number that can be represented:
0.000000001ten or 1.0ten × 10-9 (seconds in a nanosecond)
3,155,760,000ten or 3.15576ten × 109 (seconds in a typical century)

## Slide 8: Biased Exponent Representation
 Recall that exponent field is 8 bits for single precision
 E can be in the range 0 to 255
 E = 0 and E = 255 are reserved for special use (discussed later)
E = 1 to 254 are used for normalized floating point numbers
Bias = 127 (half of 254), val(E) = E – 127
 val(E=1) = –126, val(E=127) = 0, val(E=254) = 127
 How to represent a signed exponent? Choices are …
 Sign + magnitude representation for the exponent
 Two’s complement representation
 Biased representation
 IEEE 754 uses biased representation for the exponent
 Value of exponent
= val(E) = E – Bias (Bias is a constant)

## Slide 9: Biased Exponent – Cont’d
Value of a Normalized Floating Point Number is
(–1)S × (1.F)2 × 2E – Bias
(–1)S × (1.f1f2f3f4 …)2 × 2E – Bias
(–1)S × (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2E – Bias

## Slide 10: Examples of Single Precision Float
What is the decimal value of this Single Precision float?
  1 0 1 1 1 1 1 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
 Solution:
 Sign = 1 is negative
 Exponent = (01111100)2 = 124, E – bias = 124 – 127 = –3
 Significand = (1.0100 … 0)2 = 1 + 2-2 = 1.25 (1. is implicit)
 Value in decimal = –1.25 × 2–3 = –0.15625
Or Significand = (1.0100 … 0)2 X 2–3 = 0.0010100= –0.15625
What is the decimal value of?
  0 1 0 0 0 0 0 1 0 0 1 0 0 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Solution: Implicit
 Value in decimal = +(1.01001100 … 0)2 × 2130–127
= (1.01001100 … 0)2 × 23 = (1010.01100 … 0)2 = 10.375

## Slide 11: Converting FP Decimal to Binary
 Convert –0.8125 to binary in single precision
 Solution:
 Fraction bits can be obtained using multiplication by 2
 0.8125 × 2 = 1.625
 0.625 × 2 = 1.25
 0.25 × 2 = 0.5
 0.5 × 2 = 1.0
 Stop when fractional part is 0
Fraction = (0.1101)2 = (1.101)2 × 2 –1 (Normalized)
  Exponent = –1 + Bias = 126 (single precision)= 7E H
0.8125 = (0.1101)2 = ½ + ¼ + 1/16 = 13/16
1 0 1 1 1 1 1 1 0 1 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0

## Slide 12: Largest Normalized Float
What is the Largest normalized float?
  Solution for Single Precision:
0 1 1 1 1 1 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
Exponent – bias = 254 – 127 = 127 (largest exponent for SP)
  Significand = (1.111 … 1)2 = almost 2
  Value in decimal ≈ 2 × 2127 ≈ 2128 ≈ 3.4028 … × 1038
 Overflow: exponent is too large to fit in the exponent field

## Slide 13: Smallest Normalized Float
What is the smallest (in absolute value) normalized float?
 Solution for Single Precision:
0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Exponent – bias = 1 – 127 = –126 (smallest exponent for SP)
 Significand = (1.000 … 0)2 = 1
 Value in decimal = 1 × 2–126 = 1.17549 … × 10–38
 Underflow: exponent is too small to fit in exponent field

## Slide 14: Zero, Infinity, and NaN
 Zero
 Exponent field E = 0 and fraction F = 0
 +0 and –0 are possible according to sign bit S
 Infinity
Infinity is a special value represented with maximum E and
F = 0
 For single precision with 8-bit exponent: maximum E = 255
 Infinity can result from overflow or division by zero
+∞ and –∞ are possible according to sign bit S
NaN (Not a Number)
NaN is a special value represented with maximum E and
F ≠ 0
Result of exceptional situations, such as 0/0 or sqrt(negative)
 Operation on a NaN results is NaN: Op(X, NaN) = NaN

## Slide 15: Summary of IEEE 754 Encoding

## Slide 16: Floating Point Addition Example
Consider Adding (Single-Precision Floating-Point):
+ 1.111001000000000000000102 × 24
+ 1.100000000000001100001012 × 22
Cannot add significands … Why?
 Because exponents are not equal
 How to make exponents equal?
 Shift the significand of the lesser exponent right
 Difference between the two exponents = 4 – 2 = 2
 So, shift right second number by 2 bits and increment exponent
1.100000000000001100001012 × 22 = 0.01100000000000001100001 012 × 24

## Slide 17: Floating-Point Addition – cont'd
 Now, ADD the Significands:
+ 1.11100100000000000000010 × 24
+ 1.10000000000000110000101 × 22
------------------------------------------------------------------------------------------------------------------------------
+ 1.11100100000000000000010 × 24
+ 0.01100000000000001100001 01 × 24 (shift right)
-------------------------------------------------------------------------------------
+10.01000100000000001100011 01 × 24 (result)
 Addition produces a carry bit, result is NOT normalized
Normalize Result (shift right and increment exponent):
+ 10.01000100000000001100011 01 × 24
= + 1.00100010000000000110001 101 × 25

## Slide 18: Rounding
 Single-precision requires only 23 fraction bits
 However, Normalized result can contain additional bits
1.00100010000000000110001 | 1 01 × 25
Round Bit: R = 1 Sticky Bit: S = 1
 Two extra bits are needed for rounding
 Round bit: appears just after the normalized result
 Sticky bit: appears after the round bit (OR of all additional bits)
 Since RS = 11, increment fraction to round to nearest
1.00100010000000000110001 × 25
+1
----------------------------------------------
1.00100010000000000110010 × 25 (Rounded)

## Slide 19: FP Subtraction
Sometimes, addition is converted into subtraction
 If the sign bits of the operands are different
 Consider Adding:
+ 1.00000000101100010001101 × 2-6
– 1.00000000000000010011010 × 2-1
-------------------------------------------------------------------------------
+ 0.00001000000001011000100 01101 × 2-1 (shift right 5 bits)
– 1.00000000000000010011010 × 2-1
---------------------------------------------------------------------------------
0 0.00001000000001011000100 01101 × 2-1
1 0.11111111111111101100110 × 2-1 (2's complement)
-------------------------------------------------------------------------
1 1.00001000000001000101010 01101 × 2-1 (ADD)
------------------------------------------------------------------------------------
- 0.11110111111110111010101 10011 × 2-1 (2's complement)
 2's complement of result is required if result is negative

## Slide 20: Subtraction FP contnd.
+ 1.00000000101100010001101 × 2-6
– 1.00000000000000010011010 × 2-1
- 0.11110111111110111010101 10011 × 2-1 (result is negative)
 Result should be normalized
For subtraction, we can have leading zeros. To normalize, count the number of leading zeros, then shift result left and decrement the exponent accordingly.
Guard bit
- 0.11110111111110111010101 1 0011 × 2-1
- 1.11101111111101110101011 0011 × 2-2 (Normalized)
Guard bit
 Guard bit: guards against loss of a fraction bit
 Needed for subtraction, when result has a leading zero and
should be normalized.

## Slide 21: Subtraction FP contnd.
Next, normalized result should be rounded
Guard bit
- 0.11110111111110111010101 1 0 011 × 2-1
- 1.11101111111101110101011 0 011 × 2-2 (Normalized)
Round bit: R=0 Sticky bit: S = 1
 Since R = 0, it is more accurate to truncate the result
even if S = 1. We simply discard the extra bits.
- 1.11101111111101110101011 0 011 × 2-2 (Normalized)
- 1.11101111111101110101011 × 2-2 (Rounded to nearest)
Exponent -2 is biased to -2+127= 125= 7D H
IEEE 754 Representation of Result
1 0 1 1 1 1 1 0 1 1 1 1 0 1 1 1 1 1 1 1 1 0 1 1 1 0 1 0 1 0 1 1

## Slide 22: Rounding to Nearest Even
 Normalized result has the form: 1. f1 f2 … fl R S
 The round bit R appears after the last fraction bit fl
 The sticky bit S is the OR of all remaining additional bits
 Round to Nearest Even: default rounding mode
 Four cases for RS:
 RS = 00  Result is Exact, no need for rounding
 RS = 01  Truncate result by discarding RS
 RS = 11  Increment result: ADD 1 to last fraction bit
RS = 10  Tie Case (either truncate or increment result)
  Check Last fraction bit fl (f23 for single-precision or f52 for double)
  If fl is 0 then truncate result to keep fraction even
  If fl is 1 then increment result to make fraction even

## Slide 23: Floating Point Multiplication Example
 Consider multiplying:
-1.110 1000 0100 0000 1010 00012 × 2–4
× 1.100 0000 0001 0000 0000 00002 × 2–2
 Unlike addition, we add the exponents of the operands
 Result exponent value = (–4) + (–2) = –6
 Using the biased representation: EZ = EX + EY – Bias
 EX = (–4) + 127 = 123 (Bias = 127 for single precision)
 EY = (–2) + 127 = 125
 EZ = 123 + 125 – 127 = 121 (value = –6)
 Sign bit of product can be computed independently
 Sign bit of product = SignX XOR SignY = 1 (negative)

## Slide 24: FP Multiplication contnd.
 Now multiply the significands:
(Multiplicand) 1.11010000100000010100001
(Multiplier) × 1.10000000001000000000000
------------------------------------------------------------------------------------------
111010000100000010100001
111010000100000010100001
1.11010000100000010100001
10.1011100011111011111100110010100001000000000000
 24 bits × 24 bits  48 bits (double number of bits)
 Multiplicand × 0 = 0 Zero rows are eliminated
 Multiplicand × 1 = Multiplicand (shifted left)

## Slide 25: FP Multiplication contnd.
 Normalize Product:
-10.10111000111110111111001100... × 2-6
Shift right and increment exponent because of carry bit
= -1.010111000111110111111001100... × 2-5
 Round to Nearest Even: (keep only 23 fraction bits)
1.01011100011111011111100 | 1 100... × 2-5
Round bit = 1, Sticky bit = 1, so increment fraction
Final result = -1.01011100011111011111101 × 2-5
 IEEE 754 Representation
1 0 1 1 1 1 0 1 0 0 1 0 1 1 1 0 0 0 1 1 1 1 1 0 1 1 1 1 1 1 0 1

## Slide 26: Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
Double: (1 + 11 + 52)
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000